## Slide 2: 2014 Updates: Completing the New Bioterrorism Proficiency Testing Result Form and Changes to the Rule-out Algorithms
An overview of program
changes in 2014
Erin Bowles Amanda Weiss
Laboratory Network Coordinator Program Coordinator
Communicable Disease Proficiency Testing
WSLH WSLH
Phone: 608-890-1616 Phone: 608-224-4310
erin.bowles@slh.wisc.edu amanda.weiss@slh.wisc.edu

## Slide 3: Objectives
Describe the steps for logging into PT Central and entering BPE results online.
Explain how to complete a paper result form, if needed.
Identify where the revised ASM Sentinel Level Clinical Laboratory Guidelines for Suspected Agents of Bioterrorism and Emerging Infectious Diseases are located.
Notes: Slide 3 lists the objectives for today’s presentation.
At the end of the presentation you will be able to…
At the end of the presentation we will have time for any questions or comments, so please jot down any items you would like to discuss further and then bring them up at the end of the presentation.

## Slide 4: 2014 Bioterrorism Proficiency Exercise Background & Procedure Changes
Notes: Slide 4
I am going to begin today with a short review explaining why we do bioterrorism proficiency testing and then discuss some of changes made to the exercise and why they were made.

## Slide 5: Sentinel Clinical Laboratory Role in the Laboratory Response Network (LRN)
Work closely with local and state public health and federal laboratories to recognize potential agents of terrorism and other emerging threats to public health
Strength of LRN is it’s tiered
capability construct
Sentinel laboratories serve as
the foundation
  Recognize
  Rule-out
  Refer
Notes: Slide 5
You should all be very familiar with the information on this slide. This pyramid figure has been used since the beginning of the Laboratory Response Network. The Sentinel Clinical Laboratories form the base of the pyramid being the largest component of the network. The nature of the work performed by Sentinel Clinical Laboratories in performing direct patient care makes it likely that the Sentinel Clinical Laboratories will be the first to recognize and respond to a bioterrorism event, as sick patients come to the emergency department for treatment.

## Slide 6: Definition: Sentinel Clinical Laboratory
Laboratory is certified to perform high complexity testing by CLIA
Laboratory in-house testing includes Gram stains and culture of at least one of the following:
  Lower respiratory tract
  Wound
  Blood
  http://www.asm.org/images/PSAB/Sentinel-Clinical-Laboratory-Definition_2013.pdf

## Slide 7: Purpose of the Bioterrorism Proficiency Exercise (BPE)
Sentinel Clinical Laboratories are responsible for demonstrating annual competency in performing rule-out testing as outlined in the ASM “Sentinel Level Clinical Microbiology Laboratory Guidelines for Suspected Agents of Bioterrorism and Emerging Infectious Diseases”
BPE is offered free of charge to WI clinical laboratories to meet the above requirement
Notes: Start by reminding everyone of the reason why participation in BPE is important.

## Slide 8: Results of September 2013 “Rule Out” Tests for Burkholderia
Test | Sample 1: (GNR) Expected Result | % Reporting Labs | Sample 2: (GNR) Expected Result | % Reporting Labs
-hemolysis | Negative | 88.3% (of 77) | Negative | 85.7% (of 77)
-hemolysis | Negative | 89.4% (of 76) | Negative | 86.7% (of 75)
Catalase * | Positive | 34.2% (of 76) | Positive | 50.6% (of 77)
Indole * | Negative | 88.2% (of 76) | Negative | 89.5% (of 76)
Motility * | Negative | 35.1% (of 74) 1 | Positive | 47.3% (of 73)
Oxidase * | Positive | 90.8% (of 76) | Positive | 93.4% (of 76)
Urease | Positive | 21.9% (of 73) | Negative | 49.3% (of 73)
X Requirement | Not indicated | 91.5%(of 71) | Not indicated | 93.1% (of 72)
V Requirement | Not indicated | 91.5%(of 71) | Not indicated | 93.1% (of 72)
* Rule-out tests for Burkholderia
1 >50% didn’t perform testing

## Slide 9: ASM Sentinel Level Clinic Laboratory Protocols Webpage
CDC, APHL, and ASM have updated the LRN protocols which can be found at the following:
  http://www.asm.org/index.php/guidelines/sentinel-guidelines
  NEW - Introduction, General Recommendations and Biochemical Test Procedures
  Anthrax (Bacillus anthracis)
  Brucella
  Burkholderia
  Plague (Yersinia pestis)
  Tularemia (Francisella tularensis)
Notes: Also will find the Definition of LRN Sentinel Clinical Laboratories, Summary and utilization of Select Agent Forms, BT Readiness Plan, and Packing and Shipping
Revised documents, in CLSI format, have been harmonized to include the same information in each protocol in the same location.

## Slide 10: Microbiology Technology Advancements
YES - Few manual biochemicals are used by Sentinel Clinical Laboratories (SCL)
YES – Automated ID systems are the go to method for organism identification for many SCL
YES – Some SCL are using other methods to identify organisms (e.g.. Maldi-TOF, sequencing)
NO – SCL should identify BT agents
YES – SCL should rule-out BT agents
  Perform only on human clinical specimens
Notes: Committee that gathered to revise the guidelines extensively discussed changes and advances in technology for the microbiology lab.

## Slide 11: Changes to Protocols
Biosafety Levels changed to match “Biosafety in Microbiological and Biomedical Laboratories” (BMBL) and some changes to rule-out biochemicals.
  B. anthracis - BSL-2 unless working with high concentrations.
  Brucella spp. - BSL-3 (or BSL-2 with BSL-3 precautions)
  B. mallei and pseudomallei - BSL-2 for specimen processing but BSL-3 (or BSL-2 with BSL-3 precautions) for follow-up culture work & testing. Added susceptibility to amoxicillin-clavulanic acid and penicillin. Changed no pigment to no violet pigment.
  F. tullarensis - BSL-3 (or BSL-2 with BSL-3 precautions). Removed urease from rule-out test algorithm.
  Y. Pestis – BSL-2. Removed description of colonies as “fried egg” or “hammered copper” appearance. Growth slower at 37◦ than 25◦.

## Slide 12: Revised Materials
Funding cuts to emergency response
  Development of shared training and resources
    Bioterrorism Agents poster
    Bench Guides for Bioterrorism Agents
    CDC TRAIN at http://cdc.train.org
      On-line packaging and shipping refresher training
      Basic Microscopy
    Free packaging and shipping workshops for employees with no previous training

## Slide 13: Changes to BPE
Emphasis is on performing rule-out testing
No final identification is asked for
  Using an automated ID system or Maldi-TOF is not advised
Exercise is no longer designed to provide two organisms to practice the rule-out algorithm for a single bioterrorism agent (BT).
Each unknown sample may require laboratories to perform the rule-out algorithms for a different possible BT agent
Gram stain is only performed on isolate growth not primary inoculum.

## Slide 14: BPE Tips for Success
Treat as a potential BT agent, perform all work in a BSC
Subculture to Bld, Choc, MAC
Subculture isolate to Bld, Choc, MAC
Perform “rule-out” testing from 2nd subculture
Use Gram stain and growth characteristics to guide choice of rule-out algorithm to perform
Perform “Rule-out” testing - dependent on manual biochemicals available in your lab
Report what you were and weren’t able to rule out and who you would notify
Report if you would refer for further testing and where you would refer

## Slide 15: 2014 Bioterrorism Proficiency Exercise Reporting Changes

## Slide 16: Changes in 2014
REMOVED
Primary Gram stain
Final identification
ADDED
Worksheet
Online result entry
Paper result form
New Urease choices

## Slide 17: Entering Results Online
Go to the WSLH PT website: www.WSLHPT.org
Log on to PT Central
by clicking on
CLINICAL Customer Login

## Slide 18: Entering Results Online
This cover sheet will come with your samples
Enter your Login Name and Password in PT Central

## Slide 19: Entering Results Online
After logging in, you will see your HOME page

## Slide 20: Entering Results Online
Click on Bioterrorism Preparedness Exercise to view sample instructions
Click on ENTER to report your results

## Slide 21: Entering Results Online
OR
For EACH Analyte:
Comments may be added by clicking the yellow C
Select a result from each drop down menu
Select an Exception code (click yellow E)

## Slide 22: Entering Results Online
Test not indicated:
This test is not appropriate for the organism isolated
Test not performed:
This facility does not have the capability to perform this test
If a result cannot be provided:
You MUST choose either Test not indicated or Test not performed

## Slide 23: Entering Results Online
Add Comments to supplement responses
Comments are especially helpful to:
- Specify temperatures being used
- Indicate reference labs to which a patient sample would be sent

## Slide 24: Entering Results Online
Urease
For positive Urease tests
“Rapid positive” if positive at <2 hrs
“Positive” if positive at >2 hrs
New reporting option for Urea test:

## Slide 25: Entering Results Online
TEMPORARY SAVE:
Data is submitted and can be edited until the due date
FINAL SAVE:
Data is submitted and cannot be edited
SAVE your results!

## Slide 26: Building a Data Submission Report
Click on REPORTS in the upper left hand side of the PT Central screen
After results have been entered and SAVED, build a Data Submission Report for your records

## Slide 27: Building a Data Submission Report
1. Choose the Year and Event (BioterrorismPrep1)
2. Click APPLY
3. Click BUILD

## Slide 28: Questions?
See our contact information on the second slide
Call proficiency testing at 800-462-5261