## Slide 1: Rabies Diagnostics, Past, Present and Future
Rich Griesser
Wisconsin State Laboratory of Hygiene- Communicable Disease Division

## Slide 2: Rabies Diagnostics, Historical Perspective
Outline
Historical, pre-1900 identification
Virus isolation, in-vitro & in-vivo
Histopathology
Antigen detection
Molecular Methods
Lateral flow for surveillance
Antigenic & Genetic typing
Serology
Future Advances in Rabies diagnostics

## Slide 3: Rabies Diagnostics, the early days
Mosaic Esmuna Code of Babylon in 2300 B.C.
  Babylonians had to pay a fine if their dog transmitted rabies to another person
  First century A.D. Roman scholar Celsus correctly suggested rabies was transmitted saliva of the biting animal
  Utilized clinical signs in animals to “diagnose”
Animal inoculation (1804-1970s)
  Intracerebral Inoculation of dogs/rabbits with saliva from diseased animals
  Pasteur: serial inoculation of rabbits
    First vaccines in 1885
  Mouse inoculation Test(MIT)
    Webster & Dawson: increased sensitivity using Swiss mice
    Dx in 7-15 days
    Standard for routine diagnosis & still utilized as confirmatory test

## Slide 4: Rabies Diagnostics
  Histopathology
    Improved microscope technology
    1903: Aldechai Negri describes inclusions in hippocampus of rabid animals
      Intracytoplasmic inclusion bodies
      Various stains allowed for differentiation from other intracellular inclusions
      Detectable in 30-50% of cases
      Diagnostic method of choice for over 20 years
    Sellers(1927)
      Simplified technique enabling staining of fresh brain with Seller’s stain
      Testing performed in minutes
      50-80% sensitivity/specificity
      Confirmed with MIT
      Gold-standard test until DFA
    Electron Microscopy
      Confirmed viral nature of negri bodies
      Impractical & costly

## Slide 5: Rabies Diagnostics
Virus isolation, In-Vitro (1913-1990s)
  Vaccine production, research and diagnosis
  Rabies Tissue Culture infection Test (RTCIT)
    First use for isolation of virus from suspect brain material in 1970s
    Brain tissue/CSF/Saliva inoculated into MNA, BHK-21, others
    Equal or better sensitivity to MIT
    Still used by some as confirmatory test
    WHO: MIT should be replaced with cell culture for capable labs
  Limitations:
    Slow turn-around
    Lower sensitivity
    Requires technical expertise

## Slide 6: Rabies Diagnostics, Antigen Detection
Antigen Detection (1958-current)
  DFA
    Rabies virus anti-nucleocapsid IgG-FITC
    Global Gold-standard
    US National Standard Protocol 2003
    Superior Sensitivity
Limitations
  Must euthanize animal
  Requires fresh brain tissue
  Costly/limited availability of reagents
  Maintenance of cold-chain
  Expensive specialty equipment
  Low sensitivity on ante-mortem specimens(nuchal biopsy/corneal impressions)

## Slide 7: Rabies Diagnostics, Antigen Detection
Antigen Detection
  Direct Rapid Immunohistochemistry Test
    Modification of existing immunoperoxidase technique
    Rabies virus biotinylated primary antibodies & streptavidin peroxidase enzyme
    Enables use of basic light microscope and appropriate for field use
    Dx in <1 hour
Limitations
  Must euthanize animal
  Decreased sensitivity
  Kit not commercially available
  Not used for primary diagnosis in cases of public health concern
Negative DRIT test
Positive DRIT test

## Slide 8: Rabies Diagnostics, Molecular Methods for Dx
Conventional RT-PCR: N/G gene
  Time consuming
  Lower sensitivity/Poor Precision
  Result based on size discrimination
  Requires sequencing confirmation
Hemi-nested PCR
  High Sensitivity
  Requires sequencing confirmation
  High contamination risk
    False Positives?
SYBR Green real-time RT-PCR
  High sensitivity
  Dye binds any dsDNA
    Prone to non-specific amplification/False positives
    Requires sequencing confirmation

## Slide 9: Rabies Diagnostics, Molecular Methods for Dx
LN34 Taqman real-time RT-PCR
  One-step reaction
  High sensitivity
    Equal/better than hemi-nested RT-PCR
    99.90% Sensitive/99.68% specific compared to DFA
  Detects viral RNA in fresh, frozen, deteriorated and formalin fixed brain tissue
  Can detect viral RNA in ante-mortem specimens
    Serial saliva collections & nuchal skin biopsy
    Lower sensitivity in CSF, urine and Hair follicles
  Limitations: does not distinguish between lyssaviruses

## Slide 10: Rabies Diagnostics, Lateral Flow Assay
Lateral Flow Assays(LFA)
  POC test, no need for central lab
  Help with underreporting/surveillance
  Low Cost
  Widely available
  No technical expertise needed to run test
  Can accept multiple specimen types (Brain/Saliva)
  Limitations
    Many manufacturers
    Variable specificity/sensitivity
      The “good” ones may be okay for surveillance, the “bad” ones are really bad

## Slide 11: Rabies Diagnostics, Variants
In Terrestrial animals:
Unique Variant primarily transmitted among members of a single reservoir species in a defined geographic region
  Raccoons- eastern US
  NCS- Montana, Dakotas, Minnesota, Wisconsin
  SCS- Texas, Oklahoma, Kansas, Nebraska, Missouri, Louisiana
  Gray Fox x2 (unique variants)-Arizona, Texas
Sustained transmission of virus variants outside reservoir species rare(cross species transmission)
  Each CST event poses risk for viral adaptation resulting in sustained propagation in non-reservoir species
  Could result in host-shift jeopardizing rabies management efforts

## Slide 12: Rabies Diagnostics, Antigenic typing
Panel of MABs that target viral N protein
  Produced in high concentrations
  Highly conserved
Used to recognize different Rabies antigenic variants
Assess epidemiological situation
  Recognize source of outbreaks
  Identify wildlife reservoirs
Epi data allows for more efficient use of public health resources
Limitations:
  Decreased resolution in insectivorous bats
  Species identification is crucial

## Slide 13: Rabies Diagnostics, Molecular Typing

## Slide 14: Rabies Diagnostics, Molecular Typing
WSLH Approach:
  RT-PCR amplification of nucleoprotein and glycoprotein
    Current tiled WGS approaches are variant specific
    Simple 2-amplicon approach broadly amplifies all know lyssaviruses
    N & G are traditional targets, more historical data
  llumina DNA Prep library prep
  NGS on Nextseq 2000
  Align reads to reference for assembly

## Slide 15: Rabies Diagnostics, Molecular Typing

## Slide 16: Rabies Diagnostics, Molecular Typing
RABV-GLUE Analysis:
Nucleotide/Amino Acid Comparison to reference
Phylogenetic Tree with references

## Slide 17: Rabies Diagnostics, Molecular Typing

## Slide 18: Rabies Diagnostics, Serology
Not indicated for general U.S. population but Prep & serology is valuable for certain situations
Antigen function assays for detecting NA
  Rapid Fluorescent Focus Inhibition Test & Fluorescent Antibody Virus Neutralization Test
    NOT used to diagnose current infection
    Gold-standard measure of NA per ACIP/WHO
    Confirm adequate immune response to vaccination
    Pet travel
Antigen Binding tests for detecting IgG/IgM
  Indirect Immunofluorescence Assay and ELISA
    Not a measure of functional NA
    Results in hours instead of days
    Some commercial ELISA kits are available
    Large-scale screenings in populations
ACIP Risk Groups

## Slide 19: Rabies Diagnostics, Future Advances
Develop a national standard protocol mirroring DFA
Simplify molecular diagnostic methods for use in both developing & developed countries
Portable, POC molecular diagnostic testing methods under development
Lyophilized reagents to overcome cold-chain requirements
Sensitive & specific alterative isothermal molecular methods
  loop mediated isothermal amplification(LAMP)
  Recombinase polymerase amplification (RPA)
Pilot of a battery operated, chip-based real-time PCR platform in India demonstrated 92.3% specificity & 100% sensitivity to DFA
  Potential for decentralizing laboratory services by eliminating need for sample transport

## Slide 20: Rabies Diagnostics, Future Advances
Develop novel tests for ante-mortem and detection of disease prior to clinical signs
  Exome miRNA as biomarkers for infection
    Found in blood, urine, saliva, CSF
    Study: exosomal miRNAs predicted lyssavirus infection in in-vitro (neural progenitor cells) with >99% accuracy
    Further work is still needed to ensure these miRNAs are detectable in vivo at clinically relevant time points
  RPA-CRISPR
    Promising early detection assay in CSF
    As early as 3 days post-infection in rat model
    Detect 1 genomic copy in 1ul liquid

## Slide 21: Rabies Diagnostics, Future Advances
Expand Advanced molecular techniques for labs with capacity & expertise
  WGS generates detailed phylogenies that help define viral transmission in reservoir species
  Develop sequencing protocols for use in the field/developing countries
    ONT Minion
  Development of chemistries & techniques that amplify whole-genomes of all samples (fresh/fixed)
    llumina Ampliseq
    RNA from lateral flow devices
  Building of national, US-centric RABV database in CDC AMD portal
    Help with US genomic surveillance and monitoring performance of NAAT for Dx

## Slide 22: Rabies Diagnostics, Main takeaways
Rabies is an ancient disease. Diagnosis has advanced from crude, unscientific methods to highly sensitive and specific assays
Advancing diagnostic technologies allowed for production of early vaccines, for timely treatment of animal bite victims, to help investigators understand viral transmission patterns in wildlife and to aid public health investigations by identifying sources of outbreaks
The future of rabies diagnostics promises to expand highly sensitive and specific diagnostics to developing countries, offer early disease diagnosis using less invasive and ante-mortem testing, aid global rabies surveillance & control efforts and support promising experimental therapies

## Slide 23: References
https://www.cdc.gov/rabies/about/index.html
Emerging Technologies for the Detection of Rabies Virus: Challenges and Hopes in the 21st Century Fooks AR, Johnson N, Freuling CM, Wakeley PR, Banyard AC, et al. (2009) Emerging Technologies for the Detection of Rabies Virus: Challenges and Hopes in the 21st Century. PLOS Neglected Tropical Diseases 3(9): e530. https://doi.org/10.1371/journal.pntd.0000530
Faye, M., Abd El Wahed, A., Faye, O. et al. A recombinase polymerase amplification assay for rapid detection of rabies virus. Sci Rep 11, 3131 (2021). https://doi.org/10.1038/s41598-021-82479-8
Ashwini MA, Pattanaik A, Mani RS. Recent updates on laboratory diagnosis of rabies. Indian J Med Res. 2024 Jan 1;159(1):48-61. doi: 10.4103/ijmr.ijmr_131_23. Epub 2024 Mar 4. PMID: 38376376; PMCID: PMC10954107.
History of Rabies in the Americas: From the Pre-Columbian to the Present, Volume I 2023 ISBN : 978-3-031-25051-4
Laboratory techniques in rabies Volume 2 Fifth edition. Volume 2 4 February 2019 Handbook ISBN: 978 92 4 151530 6
https://www.who.int/news-room/fact-sheets/detail/rabies
Lembo, Tiziana et al. (2006). Evaluation of a Direct, Rapid Immunohistochemical Test for Rabies Diagnosis. 12(2).